## Slide 1
Andean Duct Flutes Build Packet
Musical instrument documentation capstone
Build packet: andean-duct-flutes-codex-bob-r3-build-packet
Generated: 2026-05-09
Andean Duct Flutes Build Packet | Slide 1 of 14

## Slide 2
Project Intent
• Create an L2 root-mode build packet for a small family of Andean duct flutes that can be prototyped with PVC before committing to hardwood or bamboo. The first prototype is a G4 pinkullo-style fipple flute with a removable block so the windway, window, and labium can be tuned independently from the tube.
Andean Duct Flutes Build Packet | Slide 2 of 14

## Slide 3
Physics Model
• The starting acoustic model is an open-open pipe:
f = c / (2 * L_eff) L_eff = L_physical + 2 * 0.6 * radius c = 13552 in/s at 68 F
distance_from_foot = acoustic_length * (fundamental_hz / hole_hz)
Andean Duct Flutes Build Packet | Slide 3 of 14

## Slide 4
How To Use This Packet
• Start with design.md for intent and assumptions.
• Use bom.csv, sourcing.csv, and cut-list.csv before buying or cutting.
• Use drawing-brief.md and CAD/CNC folders before machining.
• Print the packet for shopping, shop work, and validation.
Andean Duct Flutes Build Packet | Slide 4 of 14

## Slide 5
File Map
• design.md: Project intent, catalog metadata, assumptions, and validation plan.
• bom.csv: Starter bill of materials with part categories, quantities, drawing refs, and notes.
• sourcing.csv: Supplier/search tracker with specs, price/date fields, lead time, substitutes, and risks.
• cut-list.csv: Rough/final stock sizes, material, grain/orientation, operations, yield, and offcuts.
• drawing-brief.md: Manufacturing drawing and technical product sketch brief.
• assembly-manual.md: Shop-facing sequence, tools, fixtures, safety, tuning, finishing, and maintenance notes.
• validation.csv: Target/measured values, tolerance, environment, result, and tuning/build action log.
• supplier-rfq.md: Supplier email/request-for-quote starter.
Andean Duct Flutes Build Packet | Slide 5 of 14

## Slide 6
Family Spec
member_id | name | fundamental_hz | bore_id_in | od_in | physical_length_in | windway_height_in | windway_width_in | window_length_in | labium_angle_deg | scale_offsets | prototype_status
ADF-G4-P1 | Pinkullo G4 first prototype | 392.00 | 0.625 | 0.875 | 16.10 | 0.040 | 0.500 | 0.450 | 35 | 0 3 5 7 10 12 | PVC proof-of-tune
ADF-A4-P2 | Tarka A4 high prototype | 440.00 | 0.562 | 0.812 | 14.30 | 0.036 | 0.450 | 0.400 | 35 | 0 3 5 7 10 12 | queued after G4 voicing
ADF-C5-P3 | Small duct flute C5 proof body | 523.25 | 0.500 | 0.750 | 11.90 | 0.032 | 0.400 | 0.350 | 35 | 0 3 5 7 10 12 | scale experiment body
Andean Duct Flutes Build Packet | Slide 6 of 14

## Slide 7
Build Workflow
• Design and assumptions
• Source materials and hardware
• Prepare stock, fixtures, and CNC/laser/lathe setup
• Assemble, tune, finish, and validate
Andean Duct Flutes Build Packet | Slide 7 of 14

## Slide 8
Sourcing And BOM
• BOM gives part categories and drawing references.
• Sourcing tracks search terms, supplier candidates, price/date, lead time, substitutions.
• Visual BOM brief turns the parts list into a presentation-ready image board.
Andean Duct Flutes Build Packet | Slide 8 of 14

## Slide 9
Shop Packet
• Cut list for lumber/sheet/blank planning.
• Assembly manual for away-from-keyboard work.
• Validation sheet for measured dimensions, tuning, pass/fail checks.
Andean Duct Flutes Build Packet | Slide 9 of 14

## Slide 10
Drawings, CAD, CNC
• drawing-brief.md defines required views, dimensions, datums, sketch intent.
• cad/ holds models and design tables.
• cnc/ holds CAM, toolpaths, setup sheets, dry-run notes.
• drawings/ holds PDFs, SVGs, DXFs, drawing exports.
Andean Duct Flutes Build Packet | Slide 10 of 14

## Slide 11
Images And Screenshots
• Add hero render/photo, visual BOM, shop screenshots, drawing previews, validation photos in images/.
Andean Duct Flutes Build Packet | Slide 11 of 14

## Slide 12
Validation Plan
• A4 = 440 Hz reference check.
• Tuning targets logged in validation.csv.
• Critical dimensions verified against design sheet and CAD.
• Photos and revision notes after each major step.
Andean Duct Flutes Build Packet | Slide 12 of 14

## Slide 13
Open Risks / Decisions
• TBDs in design sheet and BOM.
• Supplier price/availability not yet verified.
• Generated images marked as concept placeholders.
• Empirical corrections await measured prototype data.
Andean Duct Flutes Build Packet | Slide 13 of 14

## Slide 14
Next Actions
• Replace TBDs with measured/source-backed values.
• Verify live supplier price and availability before buying.
• Export final drawings and visual BOM images.
• Regenerate this deck and print packet after final edits.
Andean Duct Flutes Build Packet | Slide 14 of 14