## Slide 1
Cajón Family
A parametric three-member box-drum family — Heifer Zephyr Instruments

## Slide 2
Project intent
• Document the cajón as a portfolio-grade parametric instrument, not as one box
• Three coordinated sizes: Compact (CJ-C), Standard (CJ-S), Bass (CJ-B)
• Four manufacturing variants per size: V1 finger-joint, V2 dovetail, V3 rabbet, V4 miter+spline
• Optional snare lineage: A none (Peruvian) / B guitar-string (flamenco) / C snare-wires
• First prototype: Standard, V1, snare option B

## Slide 3
Governing physics
• Two co-dominant resonators couple to make the bass voice
• Front-plate (1,1) clamped rectangular bending mode — the 3 mm tapa
• Helmholtz cavity with back-port — closed walnut box + 4.5″ hole
• f_H = (c/2π)·√(A/(V·L_eff)), L_eff = t_back + 1.7·(d/2)
• Standard prediction: plate (1,1) ≈ 84 Hz · cavity ≈ 96 Hz · coupled mode is the bass thump
• Risk A2: original workbook formula was missing the 1.7·r end correction

## Slide 4
Family table
• Compact: 15 × 11 × 11 in, 4.0″ hole, predicted f_H ≈ 107 Hz
• Standard ⭐: 18 × 12 × 12 in, 4.5″ hole, predicted f_H ≈ 96 Hz
• Bass: 22 × 14 × 14 in, 5.0″ hole, predicted f_H ≈ 77 Hz
• Compact runs tightly coupled (plate ≈ cavity); Bass runs cavity-dominant
• Standard sits in the middle — first-prototype target

## Slide 5
Manufacturing variants
• V1 Finger joint — table-saw jig OR CNC parametric. First-prototype default
• V2 Half-blind dovetail — CNC. Showpiece path, harder fixturing
• V3 Rabbet — table saw. Quick commercial baseline
• V4 Miter + spline — table saw + spline jig. Visual ties to inlay
• Same shell geometry, four interchangeable joinery paths
• All four variants share BOM except the joint-specific bit and feature stock

## Slide 6
CNC inlay strategy (Broinwood-derived)
• Tapered ball-nose 12.4° bit — single bit cuts pocket AND insert
• Pocket = negative in walnut body panel; insert = positive in maple
• Tapered shoulder geometry creates press-fit with no visible glue line
• VCarve allowance setting is the single tuning knob
• Route INLAY BEFORE assembly — no clamping access on a closed box
• Keep inlay within central 70% of panel; 1″ keep-out from joints

## Slide 7
Build packet
• design.md · bom.csv · sourcing.csv · cut-list.csv · validation.csv
• assembly-manual.md · supplier-rfq.md · drawing-brief.md · visual-bom-brief.md
• risks.md (17 entries, 5 categories) · wolfram-starter.wl
• drawings/ — dimensioned SVGs · cad/ — OpenSCAD master · cnc/ — bit + feed strategies
• site/ — public build-log site · scripts/ — xlsx + pptx + pdf generators

## Slide 8
Validation plan
• Predicted f_H, plate (1,1), and coupled bass per member in validation.csv
• First-prototype acceptance: f_H ±15 Hz of prediction; plate (1,1) ±15%
• Slap-vs-bass spectrum delta ≥ +5 dB at 1 kHz
• Sustain T60 between 0.30–0.55 s
• Tapa screw-torque uniformity drives plate boundary symmetry
• If cents error > 50, revisit the family scaling law (not the build)

## Slide 9
Risks (highest-leverage)
• A2: Helmholtz formula missing end-correction (corrected in design.md)
• S1: Tapa screw torque non-uniformity → asymmetric plate boundary
• SU1: 3 mm ply thickness inconsistency → plate (1,1) varies as h³
• F1: Inlay press-fit too tight cracks insert (test on scrap first)
• S4: Tapa fatigue at slap zone — long-term wear item, replaceable

## Slide 10
Next actions
• Build the Standard prototype
• Measure f_H, plate (1,1), and the slap-vs-centre spectral delta
• Update validation.csv with measured data + cents error
• If error > 50 cents, revise family scaling law in workbook
• Apply corrected Helmholtz formula to cajon-design-table.xlsx
• Generate remaining drawings (sheets 02, 04, 06, 07, 08)
• Capture build-log photography per photo-shotlist.md