## Slide 1
Ceramic Hang Capstone
Musical instrument documentation capstone
Build packet: ceramic-hang
Generated: 2026-05-06
Ceramic Hang Capstone | Slide 1 of 14

## Slide 2
Project Intent
• Design a slip-cast ceramic, handpan-inspired tonal vessel that explores raised/isolated ceramic tone fields on a shallow resonant shell. The project is a research instrument first: the goal is to learn whether molded ceramic tone fields can produce musically useful fundamentals and partials after firing, and what clay body, wall thickness, tone-field geometry, and firing schedule make that repeatable.
Ceramic Hang Capstone | Slide 2 of 14

## Slide 3
Physics Model
• This instrument is governed by coupled plate/shell vibration plus Helmholtz body resonance.
tone_field_f1 ~= (kappa / (2*pi)) * (h / a^2) * sqrt(E / (rho * (1 - nu^2)))
f_gu = c/(2*pi) * sqrt(A_gu / (V_shell * L_eff_gu)) L_eff_gu = wall + 0.6 * sqrt(A_gu/pi)
Ceramic Hang Capstone | Slide 3 of 14

## Slide 4
How To Use This Packet
• Start with design.md for intent and assumptions.
• Use bom.csv, sourcing.csv, and cut-list.csv before buying or cutting.
• Use drawing-brief.md and CAD/CNC folders before machining.
• Print the packet for shopping, shop work, and validation.
Ceramic Hang Capstone | Slide 4 of 14

## Slide 5
File Map
• design.md: Project intent, catalog metadata, assumptions, and validation plan.
• bom.csv: Starter bill of materials with part categories, quantities, drawing refs, and notes.
• sourcing.csv: Supplier/search tracker with specs, price/date fields, lead time, substitutes, and risks.
• cut-list.csv: Rough/final stock sizes, material, grain/orientation, operations, yield, and offcuts.
• drawing-brief.md: Manufacturing drawing and technical product sketch brief.
• assembly-manual.md: Shop-facing sequence, tools, fixtures, safety, tuning, finishing, and maintenance notes.
• validation.csv: Target/measured values, tolerance, environment, result, and tuning/build action log.
• supplier-rfq.md: Supplier email/request-for-quote starter.
Ceramic Hang Capstone | Slide 5 of 14

## Slide 6
Family Spec
member_id | name | outer_diameter_in | height_in | target_key | note_count | wall_target_in | gu_diameter_in | prototype_goal
CHG-P1 | Mini 3-field coupon dome | 10 | 2.75 | G minor subset | 3 | 0.24 | 2.0 | Validate tone-field geometry on a small shell.
CHG-P2 | Full blank body | 18 | 4.5 | None | 0 | 0.26 | 3.5 | Validate casting/drying/firing and gu/body mode.
CHG-P3 | Five-note vessel | 18 | 4.5 | G minor pentatonic | 5 | 0.24 | 3.5 | First musical ceramic shell.
CHG-P4 | Nine-note G minor | 18 | 4.5 | G minor | 9 | 0.22-0.30 | 3.5 | Full handpan-inspired target.
Ceramic Hang Capstone | Slide 6 of 14

## Slide 7
Build Workflow
• Design and assumptions
• Source materials and hardware
• Prepare stock, fixtures, and CNC/laser/lathe setup
• Assemble, tune, finish, and validate
Ceramic Hang Capstone | Slide 7 of 14

## Slide 8
Sourcing And BOM
• BOM gives part categories and drawing references.
• Sourcing tracks search terms, supplier candidates, price/date, lead time, substitutions.
• Visual BOM brief turns the parts list into a presentation-ready image board.
Ceramic Hang Capstone | Slide 8 of 14

## Slide 9
Shop Packet
• Cut list for lumber/sheet/blank planning.
• Assembly manual for away-from-keyboard work.
• Validation sheet for measured dimensions, tuning, pass/fail checks.
Ceramic Hang Capstone | Slide 9 of 14

## Slide 10
Drawings, CAD, CNC
• drawing-brief.md defines required views, dimensions, datums, sketch intent.
• cad/ holds models and design tables.
• cnc/ holds CAM, toolpaths, setup sheets, dry-run notes.
• drawings/ holds PDFs, SVGs, DXFs, drawing exports.
Ceramic Hang Capstone | Slide 10 of 14

## Slide 11
Images And Screenshots
• images/hero-concept.svg
Ceramic Hang Capstone | Slide 11 of 14

## Slide 12
Validation Plan
• A4 = 440 Hz reference check.
• Tuning targets logged in validation.csv.
• Critical dimensions verified against design sheet and CAD.
• Photos and revision notes after each major step.
Ceramic Hang Capstone | Slide 12 of 14

## Slide 13
Open Risks / Decisions
• TBDs in design sheet and BOM.
• Supplier price/availability not yet verified.
• Generated images marked as concept placeholders.
• Empirical corrections await measured prototype data.
Ceramic Hang Capstone | Slide 13 of 14

## Slide 14
Next Actions
• Replace TBDs with measured/source-backed values.
• Verify live supplier price and availability before buying.
• Export final drawings and visual BOM images.
• Regenerate this deck and print packet after final edits.
Ceramic Hang Capstone | Slide 14 of 14