## Slide 1
DRONE
FLUTE
FAMILY
DRN-FAM-001
Native American style
Four flutes · Walnut + Maple
Tunable drone block set
F#m · Em · Dm · Am
Tony Koop · Maker Nexus, South Bay · 2026-05-05

## Slide 2
Project Intent
What this project is, why it exists, who it's for.
A four-member family of Native American drone flutes (Am, F#m, Em, Dm). Walnut bodies with hard maple CNC inlay. Each flute ships with three swappable drone blocks — unison, fifth-below, octave-below — so the player can change drone tuning without touching the melody side.
Build it once. Tune it forever.
Inspired by elementalflutes.com gallery (drone form) and broinwood.com (CNC inlay style). Engineering reference: tonykoop/flutes — NAF K2 empirical corrections from 150+ measured flutes.
4
members
(Am · F#m · Em · Dm)
3
drone blocks per flute
(unison · 5th · octave)
8
facets per body
(octagonal CNC inlay)
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
2 / 14

## Slide 3
File Map
Every artifact in this packet.
PARAMETRIC SOURCE
Drone-Flutes-Design.xlsx — 6 sheets, 284 formulas
design.md — physics + family narrative
family-spec.csv — auto-generator input
wolfram-starter.wl — interactive notebook
sw-reference/Drone-Flutes-SolidWorks-MasterLayout.docx
STRUCTURED DATA
bom.csv · sourcing.csv
cut-list.csv · validation.csv
supplier-rfq.md (3 RFQ drafts)
drawing-brief.md · visual-bom-brief.md
risks.md (red-team failure-mode walk)
RECRUITER-FACING
capstone-deck.pptx (this deck)
print-packet.pdf (shop floor)
site/index.html (build-log site)
drawings/*.svg (4 keys + assembly + family)
inlay-patterns/ (16 DXF + 16 SVG)
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
3 / 14

## Slide 4
Build Workflow
Twelve phases over eight weeks.
1
Stock prep
2
Split-body CNC
3
Glue-up
4
Lathe round
5
CNC facet
6
Tone holes
7
Window/edge
8
CNC inlay
9
Drone blocks
10
Bird block
11
Finish
12
Tune + QA
Weeks 1–7 hands-on; week 8 cure + tune. Calendar dominated by 7-day acclimation + 7-day finish cure.
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
4 / 14

## Slide 5
Design Sheet Highlights
Drone-Flutes-Design.xlsx — single source of truth.
What it does
Six sheets, 284 formulas, all driven by one Master_Inputs sheet of named global variables. SolidWorks reads from the same Excel via a linked design table.
Edit one, change all
Drone offset is a single semitone variable. Flip from unison to fifth-below across all 4 flutes in one cell edit. Same for concert pitch (440 → 432) or bore size sweeps.
Empirical correction baked in
K2 piecewise lookup by bore_ID — five segments from −2.0% to +1.3% — applied automatically. Comes from Tony's 150+ NAF measurements.
Member | Key | f0 (Hz) | Bore | L_total
DRN-Am | Am | 440.00 | 0.750" | 21.97"
DRN-Fsm | F#m | 369.99 | 0.875" | 24.99"
DRN-Em | Em | 329.63 | 1.000" | 27.23"
DRN-Dm | Dm | 293.67 | 1.125" | 29.82"
All chamber-to-bore ratios sit in the 17–21 sweet spot.
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
5 / 14

## Slide 6
BOM & Sourcing
Materials, tooling, and where to buy.
$516
first-build total
$271 each subsequent build (tooling already on hand)
Group | Subtotal
Wood — walnut bodies + drone stock | $193
Wood — maple inlay (3 sheets) | (in $193)
Hardware + finish (Tru-Oil, glue, leather) | $78
CNC tooling — 4 bits + 8 drills (one-time) | $245
Files — generated in V-Carve | $0
Suppliers
Hardwoods to Get
Walnut S4S body blanks + drone stock
Bell Forest Products
Hard maple thin stock for inlay
IDC Woodcraft
CNC bits — solid carbide spirals
RFQ drafts ready in supplier-rfq.md — adapt contact info and send.
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
6 / 14

## Slide 7
Drawings · CAD · CNC
From parametric source to G-code.
Drawings (SVG)
Per-key dimensioned drawing
drawings/{Am,Fsm,Em,Dm}.svg
Family overview to scale
drawings/family-overview.svg
Exploded assembly
drawings/assembly.svg
Per-flute hole schedule callout
Datum chain: FOOT → WINDOW → SOCKET
SolidWorks
Master sketch on Front plane
Configurations: Am · F#m · Em · Dm
Linked design table to Excel
Global vars match Excel exactly
K2 cascade in IIF equations
DroneFlute_Master.SLDPRT
DroneFlute_Bird.SLDPRT
DroneFlute_DroneBlock.SLDPRT
CNC G-code
Generated in V-Carve from DXFs
Bore profile (1/4 downcut)
SAC pocket (1/4 downcut)
Splitting edge (1/16 upcut climb)
Faceting (1/2 downcut, V-block)
Inlay pocket (1/16 upcut)
Inlay plug (1/16 upcut, +0.001")
Tone holes (drill press)
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
7 / 14

## Slide 8
Inlay Patterns
Broinwood-inspired CNC inlay across 8 facets per flute.
Band 1 (15% from foot)
Repeating chevron · Hard maple · 0.060" deep
Band 2 (50%)
Repeating chevron · Hard maple · 0.060" deep
Band 3 (82%)
Diamond + corner dots · Hard maple · 0.060" deep
Feature panel (one facet)
7-star constellation + arrow · 0.080" deep · figured maple optional
32
inlay files
4 keys × 4 patterns × 2 formats (SVG + DXF)
96
pocket-and-plug ops to build the family
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
8 / 14

## Slide 9
Visual BOM Brief
Image-forward resource view (renders after photoshoot).
HERO IMAGE PLACEHOLDER
All 4 finished flutes laid out from longest (Dm) to shortest (Am) with drone block sets fanned out in front.
Layout reference
Header: title + quote date + estimated cost
Hero image (4 flutes + drone blocks)
Spreadsheet table from bom.csv
Thumbnails (0.75") embedded per row
3 sub-assembly callouts (right margin)
Render at 11×17 tabloid, 300 dpi
Status
Hero photo: TBD (shoot after Phase 12)
Sub-assembly renders: TBD (after Phase 9-10)
Component thumbnails: supplier images OK as placeholders
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
9 / 14

## Slide 10
Assembly Summary
Twelve-phase shop run. Full text in assembly-manual.md.
Phase 1-4
Stock & Bore
Mill walnut S4S, acclimate 7 days
Bandsaw blank in half along long axis
CNC bore + SAC + splitting-edge halves
Glue, clamp 24 h, lathe round to body_OD
Phase 5-8
Form & Finish (cuts)
V-block jig — 8 facet passes on CNC
Drill 6 tone holes from foot datum
Plunge window + finish splitting edge
Inlay 24 ops × 4 flutes = 96 pocket/plug
Phase 9-12
Assembly & QA
Lathe-turn 12 drone blocks (3/flute)
Cut + laser-engrave 4 bird blocks
Tru-Oil finish 4-6 coats; cure 7 days
Tune to ±5 cents; record validation.csv
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
10 / 14

## Slide 11
Tuning & Validation
Predictions ship; measurements feed back.
±5
cents tolerance per note
44 measurements per family
(11 notes × 4 flutes)
How validation feeds back
1
Tune each finished flute, all notes + drones, with a chromatic tuner. Record cents error.
2
Write measurement to validation.csv for that flute / note.
3
Run scripts/record_measurement.py — updates per-family corrections database.
4
If a sibling flute's prediction shifts by >2 cents, generator flags it.
5
Next family in the same lineage uses the updated K2 table automatically.
Most likely fail modes
Hole 6 (octave) sharp
Drone–melody chamber leak
Splitting edge too thick (breathy)
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
11 / 14

## Slide 12
Open Risks
Red-team failure-mode walk · risks.md
A-1
ACOUSTIC
SEV MED
Hole 6 (octave) sharp
Test: Tune-step inspection; capture per-flute correction if >+5 cents on more than 2 of 4 flutes.
A-2
ACOUSTIC
SEV HIGH
Drone–melody chamber leak
Test: Pre-glue ridge-feel check + post-glue isolated melody puff test.
S-1
STRUCTURAL
SEV HIGH
Walnut splits along glue line
Test: Same-blank halves + matched MC; Type II glue + 6+ clamps; 40-50 % RH storage.
E-1
ERGONOMIC
SEV LOW
Em/Dm hole reach for small hands
Test: 5th-percentile span check: H1↔H6 < 6" for the lower keys.
Su-2
SUPPLY
SEV MED
Walnut sapwood streaks
Test: Order with 'no visible sapwood' spec; reject deliveries >10 % sapwood by area.
F-1
FIT/FINISH
SEV LOW
Inlay flush-sand removes too much body
Test: Pre/post caliper at each band — diff must be < 0.005".
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
12 / 14

## Slide 13
Next Actions
What ships next.
1
Send the 3 RFQs (Hardwoods to Get, Bell Forest, IDC). Lock prices and lead time.
2
Acclimate walnut + maple in Tony's shop for 7 days.
3
Generate G-code in V-Carve from the SolidWorks DXFs after blanks arrive.
4
Build flute 1 (F#m, the canonical) end-to-end to validate the workflow.
5
Tune. Record measurements through record_measurement.py.
6
Photograph the 4-flute set after Phase 12 to replace the visual-BOM placeholder.
7
Publish site/ to GitHub Pages on the drone-flutes repo.
DRN-FAM-001 · Tony Koop · Maker Nexus · 2026-05-05
13 / 14

## Slide 14
Thank you
Drone Flute Family · DRN-FAM-001
Resources
GitHub repo · github.com/tonykoop/drone-flutes
Build-log site · site/index.html (in this packet)
Print packet · print-packet.pdf
Sister repos · flutes · fujara · transverse-flute · shakuhachi
Tony Koop · tonykoop@gmail.com · Maker Nexus, South Bay