## Slide 1
Title
D Kurd Handpan Root-Mode Prototype

## Slide 2
Project Intent
Create a research-grade root packet for a D Kurd handpan that is useful in the shop and honest about uncertainty. The packet supports shell procurement, fixture planning, layout, empirical tuning, validation, and private review before any public release.

## Slide 3
Instrument Context
The handpan is a coupled steel-shell idiophone with a center Ding, surrounding tuned fields, and a bottom Gu port. Its musical behavior comes from shaped steel, residual stress, tuned partials, and shell coupling.

## Slide 4
Source Artifacts
The starting design comes from `handpan-design-table.xlsx`, sheet `Handpan`, with a 21 in shell, 1.0 mm steel, 3.5 in Gu, A=440, and a D Kurd 9-note layout.

## Slide 5
Physics Model
The packet uses plate and Helmholtz formulas as first-order sanity checks only. Final pitch is determined by measured hammered geometry, work-hardening, boundary conditions, field coupling, and tuner decisions.

## Slide 6
Scale And Layout
The target root mode is D Kurd: D3 Ding with A3, Bb3, C4, D4, E4, F4, G4, and A4 surrounding fields. The oval field sizes are removable-template starters, not final acoustic contours.

## Slide 7
Manufacturing Strategy
The first build should use purchased or professionally formed shells. CNC and CAD are used for support rings, templates, drawings, and inspection aids rather than final tuned tone-field geometry.

## Slide 8
Tuning Workflow
Tune the Ding first, then move from low fields to high fields. Each field is measured for fundamental, octave, and compound fifth, and each change triggers a recheck of previously tuned fields.

## Slide 9
Validation Plan
Acceptance is tuner-driven: cents error, overtone behavior, sustain, cross-talk, Gu response, and retuning drift are logged across rough tuning, shell closure, final tuning, and one-week rest cycles.

## Slide 10
Risks
Major risks include metal-forming hazards, heat-treatment distortion, tuning repeatability, false precision in formulas, adhesive/rim effects, and premature public release. These are documented in `risks.md`.

## Slide 11
Private Review Gate
The handpan should stay private until a human tuner and metal-forming reviewer approve the process and measured data. The packet is a disciplined prototype handoff, not a finished-instrument guarantee.

## Slide 12
Deliverables
The repo now includes design, BOM, sourcing, cut list, validation, assembly, RFQ, drawing/CAD/CNC briefs, visual BOM brief, Wolfram starter, risks, photo shotlist, print packet, site, and capstone manifest artifacts.

## Slide 13
Next Actions
Source or inspect a practice shell, verify supplier data, build the tuning frame and templates, run coupon tests, and begin a measured tuning log before committing the final shell pair.