## Slide 1
Hulusi (葫芦丝)
Wooden Cucurbit Free-Reed Flute Family
B♭ · C · D · F · G — five keys, one parametric workbook
HUL-001 · v4.1 instrument-maker scaffold · capstone deck
Stopped-pipe + free-reed acoustic model · 33 named globals · SolidWorks parity
github.com/tonykoop/hulusi · Tony Koop · Maker Nexus South Bay

## Slide 2
What this is
Engineering documentation for a 5-key family of wooden hulusi — the Chinese cucurbit free-reed flute.
1
Parametric design table
33 named global variables in Master_Inputs drive 6 derived sheets. SolidWorks design-table parity matches names exactly. 113 formulas, 0 errors.
2
Complete v4 build packet
BOM · sourcing · cut-list · validation · assembly manual · drawing brief · risks (red-team) · family-spec · photo shotlist · supplier RFQ.
3
Recruiter-grade artifacts
12-slide capstone deck · printable shop PDF · self-contained build-log site · concept renders that step aside for shop photos.
First prototype: F-key (modern factory standard, all-closed = F4 = 349 Hz). Family scales from there.
2 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 3
Physics
Three independent stopped-pipe + free-reed systems sharing a wind chest.
Stopped pipe
f = c / (4 · L_eff)
Each tube acts as a stopped pipe — closed at the reed, open at the foot.
L_eff = L_acoustic + 0.6·r_bore
End correction at the open foot only. Default c_speed = 13,552 in/s @ 68°F.
Free reed (cantilever)
f_reed = K · t / L²
Brass C26000 tongue clamped at root, free at tip; oscillates against frame slot.
K_imperial ≈ 27,300
Tongue cut sharp by pull_down_cents (default −30¢). Tube pulls reed down to its resonance.
Finger holes
d = L · (f₀ / f_n)
Each opened hole shortens the effective length per the simple shortening rule.
Default offsets: 2 4 5 7 9 11 12
Western diatonic; traditional Chinese tuning reachable by editing semitone column.
All three live in Master_Inputs as named global formulas — change c_speed once, all 5 family rows update.
3 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 4
File map
v4.1 Mode A (single-instrument repo at root) — 24 deliverable files plus images.
Top-level docs
README.md
v4 hero + status table
design.md
physics + lineage + ladder
risks.md
red-team, 5 categories × tests
LICENSE
MIT
v4-audit.md
audit trail vs v4 spec
Parametric design
hulusi-design-table.xlsx
Master_Inputs + 6 sheets
family-spec.csv
5 keys, one row each
cad/hulusi_master.scad
OpenSCAD parametric
cad/hulusi-design-table.txt
SW global-var parity
wolfram-starter.wl
physics sanity-check
Build packet
bom.csv
15 line items
sourcing.csv
supplier candidates
cut-list.csv
12 cuts + family scaling
validation.csv
target/measured/cents-error
assembly-manual.md
14-step shop sequence
supplier-rfq.md
copy-paste RFQ
Visual + recruiter
drawings/hulusi-{Bb..G}.svg
5 per-key dimensioned
drawings/hulusi-section.svg
centerline section
drawings/reed-detail.svg
reed slot 4×
photo-shotlist.md
14 build-log shots
site/index.html
build-log static site
capstone-deck.pptx + print-packet.pdf
this deck + shop PDF
4 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 5
Master_Inputs — single source of truth
33 named globals · blue inputs · every other cell is a formula · names match SolidWorks 1:1.
Master_Inputs
ACOUSTIC CONSTANTS
Speed of sound (in/s, 68°F)
13552
c_speed
KEY (selectable)
Selected key MIDI
65
key_midi
Tonic frequency (derived)
349.23
f_tonic
MELODY PIPE (7 holes)
Bore ID (in)
0.500
mel_bore_ID
Hole diameter (in)
0.275
mel_hole_dia
REED (brass C26000)
Shim thickness (in)
0.008
reed_thickness
K constant (imperial)
27300
reed_K_imperial
EMPIRICAL CORRECTIONS
Reed pull-down (¢)
−30
pull_down_cents
Pipe correction (%)
0.0
correction_pct
33
named global variables
shared with SolidWorks
113
live formulas across
6 derived sheets
0
formula errors after
LibreOffice recalc
Sister: cad/hulusi-design-table.txt — SW parity reference.
5 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 6
Family — five keys, one workbook
Change key_midi once. Family sheet recomputes mel/dr1/dr2 lengths and reed-tongue lengths for all 5 keys.
Model
Key
Tonic Hz
Mel L
Dr1 (5th) L
Dr2 (oct) L
Reed L mel
Use
HUL-B♭
B♭
175 Hz (F3)
14.89 in
10.05 in
7.62 in
0.977 in
low / warm voice
HUL-C
C
196 Hz (G3)
13.30 in
8.99 in
6.82 in
0.922 in
vocal / intermediate
HUL-D
D
220 Hz (A3)
11.89 in
8.05 in
6.12 in
0.871 in
folk / dance pieces
HUL-F ★
F
262 Hz (C4)
10.05 in
6.82 in
5.20 in
0.798 in
STANDARD — prototype 1
HUL-G
G
294 Hz (D4)
8.99 in
6.12 in
4.67 in
0.753 in
bright / festive
★ F-key = HUL-P2 prototype 1 (in flight). All other keys deferred until F-key voicing locks.
14.9″
B♭
13.3″
C
11.9″
D
10.1″
F ★
9.0″
G
6 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 7
Drawings & CAD
Per-family-member dimensioned SVGs (B♭/C/D/F/G) plus section, family-scale, reed-detail.
Centerline section
Gourd + 3 pipes + reed slot. Critical wall thickness, bore ID, pipe-axis angles.
Family scale
All 5 keys side-by-side at 1:18 px scale. Dimension labels per key from family-spec.csv.
Reed slot detail (4×)
Tongue, frame plate, slot, glue line, wax fillet. Cantilever model with K = 27,300.
CAD pipeline: Master_Inputs → SolidWorks global vars → parametric model → SVG drawings → ShopBot/laser/lathe
OpenSCAD master at cad/hulusi_master.scad mirrors the SW parametric structure for hobbyist build path.
7 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 8
BOM & sourcing
15 line items per F-key build · ~$80–100 in materials · all parts sourced from named suppliers.
Wood
$30–45
Walnut gourd blank (1) · Pakkawood tubes ×3
Brass
$25–35
Shim 0.008″ × 1 sheet · Plate 0.040″ × 1 sheet
Sealant
$15–25
Beeswax (food grade) · Pine rosin (violin)
Hardware
$10–25
Boxwood mouthpiece · Brass binding ring
Tooling
$15–25
Reed needle-file set · (one-time, reusable)
Test
$0–30
Tuner / mic · (smartphone OK)
Per-build cost
$95
median F-key build
Suppliers (sourcing.csv)
• Cousineau Wood Products
• Bell Forest Products
• McMaster-Carr
• Stewart-MacDonald
• Frontier Natural / local
Substitution rules in sourcing.csv. Family scaling adds ~$70/key in additional wood + brass beyond the F-key build.
8 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 9
Build workflow
14 shop steps. Prototype ladder runs P0 → P4 across 4–6 weeks of evening builds.
P0
Reed coupon
validate brass-cut + slot fit
1 evening
P1
Single melody pipe
validate stopped-pipe + holes
1 weekend
P2
Full F-key hulusi
hit family target (prototype 1)
2 weekends
P3
Waxable Drone 2
removable-wax drone control
1 evening
P4
Family scaling
B♭/C/D/G additional builds
ongoing
Full 14-step shop sequence in assembly-manual.md. Each step has failure-mode notes.
9 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 10
Validation & empirical loop
Two correction knobs — pull_down_cents (per-reed) and correction_pct (global pipe scale) — close the loop.
Predict
Master_Inputs formulas
Build
ShopBot + lathe + Epilog
Measure
validation.csv tuner Hz
Correct
pull_down_cents correction_pct
Each new measurement updates the next build's targets — eventually every key prints to ±15¢ predicted.
10 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 11
Open risks (red team)
18 tracked risks across 5 categories. Every risk has a verification test attached.
A1 — Reed pull-down assumption
−30¢ default may be wrong by ±20¢. Whole reed family cuts to wrong target.
✓ Test: HUL-P0 measured pull-down vs predicted.
HIGH
S3 — Gourd glue-line failure
Two-half hollow gourd: humidity + pressure stresses can pop the joint.
✓ Test: vacuum pressure-test at 30/60/90 days.
HIGH
S1 — Pakkawood splits during boring
Resin can soften, gum the bit, or split along grain.
✓ Test: 3 consecutive bores complete with no splits.
MED
E1 — Hand-fit ergonomics
F-key hole span (3.7″) may not fit small hands.
✓ Test: 3 players, large/avg/small hand, scale played without strain.
MED
Full risk register at risks.md — 18 entries · 5 categories · acoustic, structural, ergonomic, supply, fit/finish.
11 / 12
Hulusi (葫芦丝) family · v4.1 build packet · 2026-05-05

## Slide 12
Next actions
Documentation complete. The HUL-P0 reed coupon is the first physical step.
This week
HUL-P0 reed coupon
Cut 3 brass tongues on Epilog. Sound off-pipe; measure free frequency.
→ Validates A1 (reed pull-down) + A2 (K constant).
Next week
HUL-P1 melody pipe
Bore one pakkawood tube, drill 7 holes, mount reed. Validate stopped-pipe model.
→ Validates S1 (boring), full hole layout.
Month 2
HUL-P2 full F-key build
Lathe gourd, assemble three pipes, full acoustic test. Hit family target.
→ Validates S3 (gourd glue), full system.
Month 3+
Family scaling
Once F-key voicing locks, scale to B♭/C/D/G using same workflow.
→ Documents per-key calibration in validation.csv.
github.com/tonykoop/hulusi · v4.1 instrument-maker scaffold · ready for HUL-P0