## Slide 1
Sambuca
A modern boat-shaped arched harp
inspired by the Royal Cemetery of Ur, c. 2600 BC
SAM-13-ROOT prototype + parametric family of five variants
Tony Koop · Heifer Zephyr · Fall 2026 capstone

## Slide 2
Where this instrument comes from
And what that gives us.
The artifact
BM 121198, Royal Cemetery at Ur, c. 2600 BC.
British Museum curator's card: "more accurately described as a boat-shaped harp" — not a lyre.
Surviving Sumerian material: gold tuning pegs and lapis lazuli decorations. The wood is a 1971–72 reconstruction.
What that means
The visual fingerprint is locked.
Everything underneath is design freedom.
Inspired by the Sumerian pattern — not a reproduction of any specific artifact, not a claim against any modern living tradition.
Sambuca · Fall 2026 capstone · private review

## Slide 3
Fingerprint preservation
Eight elements that read as Sumerian sambuca.
Gold-flared cap at the neck top.
13 bulb-headed tuning pegs with visible cord wraps.
Strong J-curve neck.
Multi-strip lapis band along the soundboard-hull seam.
Brass collar at the neck-body joint.
Slim boat hull with pronounced bow lift.
Rectangular pale inlay panel at the bow end.
Two integral stub blocks at the stern keel.
Sambuca · Fall 2026 capstone · private review

## Slide 4
What I'm modernizing
Where the build departs from the pattern.
Soundhole at the keel, not the soundboard — projects sound away from the player toward the listener.
Geared guitar tuners hidden inside the neck, behind PVD-gold-tone bulb caps and decorative cord wraps.
Modern strings — fluorocarbon trebles + wound nylon basses, 65–80 kgf calibrated total.
CNC fabrication for the hull, neck, inlay, and stand.
Japanese kanawa-tsugi joinery on the stand — a stylistic choice, not Sumerian.
Sambuca · Fall 2026 capstone · private review

## Slide 5
Family spec
One MasterLayout, five buildable variants.
Sambuca · Fall 2026 capstone · private review
ID | Body length | Strings | Tuning range | Harness | Role
SAM-13-ROOT | 650 mm | 13 | G3 → E5 | none | build target
SAM-19-MID | 850 mm | 19 | D3 → G5 | low-back belt | mid concert
SAM-25-CONCERT | 1050 mm | 25 | A2 → A5 | sax harness | concert
SAM-13-AE | 650 mm | 13 | G3 → E5 | none | acoustic-electric
SAM-13-MULE | 650 mm | 13 | G3 → E5 (reduced T) | none | tension test mule
All five share one parametric MasterLayout. body_length_mm and string_count drive the configurations.

## Slide 6
Parametric SolidWorks workflow
One equations file, one design table, five buildable instruments.
Sources of truth
cad/SAM-000_master-equations.txt — global equations.
SolidWorks Equations Manager binds every dimension by name.
Design table drives 5 configurations from 4 anchor parameters.
Driving parameters
body_length_mm (650 / 850 / 1050)
string_count (13 / 19 / 25)
f_min_hz, f_max_hz (tuning anchors)
scale_factor derives the rest
Sambuca · Fall 2026 capstone · private review

## Slide 7
Acoustic study results
Predicting and validating the voice.
What Wolfram predicts
3.8 L hull cavity — small.
Keel-port Helmholtz: ~143 Hz.
First plate mode (cedar @ 3 mm): ~160 Hz.
Coupled cavity-plate pair: ~125 Hz / ~185 Hz.
Bass strings sit just above the lower coupled mode — the voicing sweet spot.
How we'll validate
Sweep frequency response on the SAM-13-MULE.
SPL measurement at 1 m with calibrated mic.
Tolerance: predicted ±6 dB.
Escalation paths: thinner cedar, larger port, or pickup configuration.
Sambuca · Fall 2026 capstone · private review

## Slide 8
Inlay program
Multi-strip lapis band + bow inlay panel, all CNC-driven.
Multi-strip lapis band: 5 parallel strips × 1.5 mm dyed-blue veneer with 0.8 mm light spacers (~12 mm total band width).
Single-pass CNC route with a 0.8 mm end mill — same setup as the bow-panel pocket.
Bow-end inlay panel: 100 × 60 mm pale rectangular panel framing the string-anchor zone (mother-of-pearl or shell composite).
Inlay program is parametric — scales with scale_factor for SAM-19 and SAM-25.
Brand integration (Heifer Zephyr wordmark) is added in a separate inlay pass once Option A (soundboard) or Option B (stand) is locked.
Sambuca · Fall 2026 capstone · private review

## Slide 9
Build sequence
12 stages, 60–90 hours of active build time over 6–10 weeks.
Stages
Stage 1: hull (CNC-from-block or stave-laminated).
Stage 2: neck (3-laminate sapele, CNC sweep).
Stage 3: soundboard with inlay pockets.
Stage 4: scarf joint + brass collar.
Stage 5: soundboard installation + inlay.
Hold points
Stage 9: string-holder strip voicing on the MULE.
Stage 10a: 30-day MULE tension hold — public-release gate.
Stage 10b: SAM-13-ROOT gradual stringing to 65–80 kgf.
Stage 11: acoustic measurement vs prediction.
Sambuca · Fall 2026 capstone · private review

## Slide 10
Validation gates
Three blockers between private review and public release.
Structural — SAM-13-MULE 30-day neck-deflection hold under reduced tension. Pass criterion: ≤2 mm deflection at the gold cap.
Cultural — advisor review of the provenance language. Sumerian pattern is public domain; the sambykē etymological link is honestly flagged as historically contested.
Brand — Heifer Zephyr wordmark placement option (A soundboard vs B stand) locked.
Sambuca · Fall 2026 capstone · private review

## Slide 11
Cultural provenance language
The public-release standard, locked.
Inspired by the Sumerian pattern (~4500 years old, public domain).
Not a reproduction of any specific surviving artifact.
Not a recreation of any reconstructed instrument such as BM 121198.
Not a claim of cultural authority over any modern living tradition.
Sambykē (σαμβύκη) etymological link to the Sumerian form is historically contested. This build adopts "sambuca" while acknowledging the uncertainty.
Sambuca · Fall 2026 capstone · private review

## Slide 12
Finished prototype
SAM-13-ROOT, finished, tuned, played.
[HERO-01 — SAM-13-ROOT three-quarter on stand, soft directional light]
"Acoustic harp inspired by a pattern 4500 years older than this room, built with CNC and tuned for the room you'd play it in."
Sambuca · Fall 2026 capstone · private review

## Slide 13
What I learned
Three honest takeaways.
The string-holder strip belongs in arched-harp practice; the "bridge bar" was a kora-pattern leak that almost cost me a wrong build. Reverse-engineering happened in real time during this packet build.
Coupled cavity-plate analysis predicts voice more accurately for arched harps than the single-cavity model I started with.
"Fingerprint preservation, modernize everything else" framing scales. It works for the sambuca, and would work for any pattern instrument with surviving fragments + interpretive wood.
Sambuca · Fall 2026 capstone · private review

## Slide 14
What's next
The roadmap from prototype to release.
Before release
Cultural advisor review (in progress).
SAM-13-MULE build for tension validation.
Brand integration option locked.
Then
Public release with site/index.html + GitHub repo + capstone showing.
SAM-19-MID and SAM-25-CONCERT queued for 2027.
Learn-to-play songbook (paired with the sheet-music skill).
Sambuca · Fall 2026 capstone · private review

## Slide 15
Credits & sources
Where this came from, who's owed credit.
British Museum object 121198 — © Trustees of the British Museum, CC BY-NC-SA 4.0. Photos by Don Hitchcock, 2015.
Herbology Manchester supplemental profile photo.
Penn Museum object 47880 / B16728 — courtesy Penn Museum, University of Pennsylvania.
Kora MasterLayout as parametric template (C:\Users\Tony\Documents\GitHub\kora).
Heifer Zephyr workshop, Maker Nexus shop access.
Tony Koop, with the instrument-maker-v4 skill from Anthropic.
Sambuca · Fall 2026 capstone · private review