## Slide 1: Project Intent
Publish the sheng split from issue #153 and the tonykoop/sheng issue #1 starter packet as two explicit packet variants without forcing a premature architecture winner.

## Slide 2: Branch Decision
The first decision is traditional-side-branch versus compact-control.

## Slide 3: Traditional Branch
Traditional side-branch rows use side_branch_reed with end_condition=both_ends_open.

## Slide 4: Compact Branch
Compact control rows use closed_open with end_condition=one_end_closed_reed.

## Slide 5: Family Spec
Each branch has its own family-spec.csv. The sheets must stay separate unless measurements prove a shared acoustic model.

## Slide 6: Coupon Gate
The P0 reed coupon records reed-alone pitch, onset pressure, blow/draw behavior, gap, window size, pull-down behavior, retention, and leak status.

## Slide 7: Single-Pipe Gate
One measured single-pipe control comes before any full mouth-organ body layout.

## Slide 8: Windchest Gate
Chamber volume, pressure tap, gasket land, inlet, service access, and leak method stay in planning tables until measured evidence exists.

## Slide 9: Drawing Authority
Future DXF/CAD must name branch, reed window, socket map, gasket land, windchest section, and service direction.

## Slide 10: Visual Authority
Generated images are concept or reference support only.

## Slide 11: Fabrication Status
Current status is scaffold. This packet is not build-ready.

## Slide 12: Risks
The primary risks are unmeasured reed behavior, chamber leakage, unsafe pressure testing, and accidental branch mixing.

## Slide 13: Next Actions
Pick a branch, fill the P0 coupon and safety gates, build one single-pipe control, run chamber leak checks, then revise the selected branch sheet with measured evidence.