## Slide 1
HEIFER ZEPHYR
Siku (Zampoña)
Andean Panpipe — Four-Member Family
instrument-maker-v4 · packet v4.3 · 2026-05-08
HEIFER ZEPHYR

## Slide 2
Project Intent
The siku is the Andean panpipe — one of the oldest continuously played instruments in the world, with archaeological specimens from Tiwanaku and Nazca dated to at least 1500 BCE.
The Instrument
Played in interlocking arka/ira pairs. Neither rank alone contains the full scale — two players weave a melody together, embodying yanantin: the Aymara philosophy of complementary pairing.
This Build
A four-member family (Toyo/Zanka/Malta/Chili) using parametric acoustic design, CNC-routed cherry frame rails, and bamboo or PVC tubes. Primary target: Zanka (key of C, tenor voice).
Goal: A fully-documented, reproducible build packet for the complete siku family, publishable as a GitHub portfolio instrument and buildable from this packet alone.
HEIFER ZEPHYR

## Slide 3
Yanantin
The Aymara Philosophy of Complementary Pairing
ARKA ♀ Leader
7 tubes · semitones 0 4 7 10 14 17 21
G3
B3
D4
F4
A4
C5
E5
Carries the lead phrase
IRA ♂ Follower
6 tubes · semitones 2 5 9 12 16 19
A3
C4
E4
G4
B4
D5
Answers the lead phrase
Neither rank alone contains the full scale. Together: G Mixolydian.
HEIFER ZEPHYR

## Slide 4
Instrument Family
Toyo
Bass · G3
bore 0.750"
OD 1.000"
longest 22.6"
frame 13.75"
PRIMARY BUILD
Zanka
Tenor · C4
bore 0.625"
OD 0.821"
longest 16.96"
frame 11.42"
Malta
Alto · G4
bore 0.500"
OD 0.658"
longest 11.3"
frame 9.30"
Chili
Soprano · A4
bore 0.375"
OD 0.493"
longest 7.6"
frame 7.16"
HEIFER ZEPHYR

## Slide 5
Acoustic Design
L_calc = 13552 / (4 × f_hz) − 0.82 × bore_ID
L_cut = L_calc + 3/16" (tuning trim allowance)
Parameter | Value | Notes
Speed of sound | 13,552 in/s | At 68°F shop standard
End correction | 0.82 × bore_ID | Empirical — bundles embouchure effects
Pipe type | Stopped cylindrical | Odd harmonics only: 1f, 3f, 5f…
Tuning | A4 = 440 Hz | Equal temperament
Trim allowance | 3/16" (0.1875") | All L_cut values include this margin
Sanity check — Zanka A4: L_calc(440 Hz, bore=0.625") = 13552/(4×440) − 0.82×0.625 = 7.188" ✓
HEIFER ZEPHYR

## Slide 6
Zanka Tube Layout — G3 to E5
G3
A1
A3
I1
B3
A2
C4
I2
D4
A3
E4
I3
F4
A4
G4
I4
A4
A5
B4
I5
C5
A6
D5
I6
E5
A7
Arka (7 tubes, leader ♀)
Ira (6 tubes, follower ♂)
HEIFER ZEPHYR

## Slide 7
Tube Cross-Sections — All Four Members
Toyo
G3 Bass
bore 0.75"
OD 1" wall 0.125"
Zanka
C4 Tenor
bore 0.625"
OD 0.821" wall 0.098"
Malta
G4 Alto
bore 0.5"
OD 0.658" wall 0.079"
Chili
A4 Soprano
bore 0.375"
OD 0.493" wall 0.059"
End correction (open end only): ΔL = 0.82 × bore_ID | Stopped pipe: odd harmonics only (1f, 3f, 5f…)
HEIFER ZEPHYR

## Slide 8
Frame Rail & Binding
TOP RAIL
BOTTOM RAIL
Parameter | Value
Material | Cherry or walnut S4S 3/4" × 1.5"
Pocket width | OD − 0.005" (light interference fit)
Pocket depth | OD / 3
Pocket pitch | OD + 1/16" center-to-center
Binding cord | Waxed linen or nylon, 1 mm
Wraps per tube | 3 minimum; square-knot at ends
Glue | Thin film in pockets (optional)
No hardware — only wood, bamboo/PVC, beeswax, and cord.
HEIFER ZEPHYR

## Slide 9
Build Sequence — 8 Phases
1
Stock Verification
Measure bore ID + OD of all incoming stock; record in validation.csv
2
Tube Cutting
Story stick (bamboo) or digital stop (PVC); 52 tubes; label immediately
3
Closed-End Sealing
Beeswax pour in plywood fixture; 3/8" depth; 30 min cure
4
First Tuning Pass
Measure all tubes; record cents deviation in validation.csv
5
Frame Rail Fabrication
CNC-route 13 pockets; pocket width = OD − 0.005"; dry-fit before glue
6
Assembly & Binding
Seat tubes; waxed cord wrap; 3+ passes per tube; square-knot finish
7
Trim-Tuning
File/saw open ends to ±5 cents; update validation.csv same session
8
Finishing
Danish oil on rails; tung oil wipe on bamboo; photograph
HEIFER ZEPHYR

## Slide 10
Manufacturing Notes
Tube Boring Method by Member
Member | Method | Max Tube Length | Key Constraint
Toyo | Headstock-driven deep bore | 22.6" | Prevents drill wander at depth
Zanka | Lathe tailstock drill | 17.0" | 4-jaw chuck; steady rest >12"
Malta | Drill press + V-block | 11.3" | Forstner or brad-point bit
Chili | Drill press + V-block | 7.6" | Single clamp sufficient
Jig Build Priority
Priority | Jig | When Needed
P1 | Story stick × 4 (one per member) | Before any cutting
P1 | Sealing stand × 4 (one per member) | Before Phase 3 sealing
P2 | CNC pocket toolpath | Before Phase 5 frame fabrication
P3 | Tailstock carrier for deep bore (Toyo only) | Before boring hardwood Toyo blanks
HEIFER ZEPHYR

## Slide 11
Materials Summary
Member | Tubes | Frame Rails | Plugs | Cord | Est. Total
Toyo (Bass) | $6.50 | $12.00 | $1.30 | $0.25 | ~$20
Zanka (Tenor) | $5.20 | $10.00 | $1.04 | $0.20 | ~$17
Malta (Alto) | $4.55 | $8.00 | $0.78 | $0.15 | ~$14
Chili (Soprano) | $3.90 | $7.00 | $0.65 | $0.10 | ~$12
Shared Tools (once)
Chromatic tuner: $15
Beeswax block: $3
Abrasive paper: $2
Danish oil: $8
Total shared: ~$28
Single Zanka Build
~$17 materials + $28 shared tools
= ~$45 for first build
Full four-member family: ~$91
(excludes finish and consumables)
HEIFER ZEPHYR

## Slide 12
Key Risks
H
AC-04
Chili Arka-7 (F#6, 1.982") borderline playable
Build as 11-tube Chili; omit top 2 tubes
M
AC-01
Bamboo bore variance (±0.015" typical)
Measure all tubes before cutting; adjust L_calc per measured bore
M
AC-02
Temperature drift (±10°F → ±0.9% pitch)
Tune and play at same temperature; note shop temp in validation.csv
M
ST-01
Rail pocket undersize causing tube cracking
First pocket is always a test pocket; verify fit before batch routing
H
ER-01
Yanantin not explained in public documentation
See resources.md §Provenance; required before any public publish
Full risk register: 11 risks in risks.md
HEIFER ZEPHYR

## Slide 13
Packet Contents
design.md
Design doc, tube length tables, arka/ira split
family-spec.csv
4 members, 13 tubes each, all parameters
bom.csv
Full bill of materials (29 rows)
cut-list.csv
52 tube cuts + 4 rail cuts
validation.csv
Per-tube targets: Hz, cents tolerance
assembly-manual.md
8-phase build manual with tool list
risks.md
11 structured risks with verification tests
cnc/setup-sheet.md
Machine datums, tooling, release checks
wolfram/instrument-model.wl
Interactive tube-length explorer
drawings/ (10 SVGs)
Dimensioned drawings: elevation, cross-section, details
site/index.html
Build-log site with live tube visualiser
print-packet.pdf
5-page printable shop reference
HEIFER ZEPHYR

## Slide 14
Open Items
OI-01 · H
Photos: all 36 shots in photo-shotlist.md pending actual build. HERO-03 (Zanka arka beauty shot) is the README hero image.
OI-02 · M
Chili Arka-7 prototype: build and test the 1.982" F#6 tube before committing full Chili production (resolves risk AC-04).
OI-03 · M
Wolfram audio recordings: capture AudioGenerator output for arka + ira ranks; embed in build-log site.
OI-04 · L
OpenSCAD model: cad/siku-openscad-starter.scad is TBD per drawing-brief.md.
OI-05 · L
Sourcing confirmation: verify current bamboo cañahueca availability; lead time 2–4 weeks for import suppliers.
OI-06 · L
Validation.csv: fill in measured_hz column after first Zanka prototype build and confirm ±5 cent tolerance.
HEIFER ZEPHYR

## Slide 15
Cultural Provenance
Attribute accurately
Describe as "Andean Aymara/Quechua in origin" — not "Incan" or "South American"
Don't claim authenticity
This is a contemporary workshop interpretation — state this clearly in README and public docs
Explain yanantin
The interlocking duet is not decorative; it embodies a cultural philosophy of complementary pairing
Don't sell as traditional
The CC BY 4.0 license covers the engineering documentation, not the cultural tradition
Primary reference
Thomas Turino — Moving Away from Silence (Chicago, 1993)
tonykoop/siku-zampona · CC BY 4.0 · Heifer Zephyr · packet v4.3