## Slide 1
Vessel Flutes Build Packet
Musical instrument documentation capstone
Build packet: vessel-flutes-codex-bob-r3-build-packet
Generated: 2026-05-09
Vessel Flutes Build Packet | Slide 1 of 14

## Slide 2
Project Intent
• Create an L2 root-mode build packet for vessel flutes whose pitch behavior is set by Helmholtz resonance. The first prototype is a 130 cc ceramic ocarina lab body with a conservative voicing and undersize finger holes. The purpose is to validate cavity volume, voicing response, cumulative hole area, and shrinkage before committing to a polished slip-cast family.
Vessel Flutes Build Packet | Slide 2 of 14

## Slide 3
Physics Model
• Helmholtz resonance:
f = c / (2*pi) * sqrt(A / (V * L_eff)) L_eff = wall_thickness + end_correction end_correction ~= 0.6 * sqrt(A/pi)
Vessel Flutes Build Packet | Slide 3 of 14

## Slide 4
How To Use This Packet
• Start with design.md for intent and assumptions.
• Use bom.csv, sourcing.csv, and cut-list.csv before buying or cutting.
• Use drawing-brief.md and CAD/CNC folders before machining.
• Print the packet for shopping, shop work, and validation.
Vessel Flutes Build Packet | Slide 4 of 14

## Slide 5
File Map
• design.md: Project intent, catalog metadata, assumptions, and validation plan.
• bom.csv: Starter bill of materials with part categories, quantities, drawing refs, and notes.
• sourcing.csv: Supplier/search tracker with specs, price/date fields, lead time, substitutes, and risks.
• cut-list.csv: Rough/final stock sizes, material, grain/orientation, operations, yield, and offcuts.
• drawing-brief.md: Manufacturing drawing and technical product sketch brief.
• assembly-manual.md: Shop-facing sequence, tools, fixtures, safety, tuning, finishing, and maintenance notes.
• validation.csv: Target/measured values, tolerance, environment, result, and tuning/build action log.
• supplier-rfq.md: Supplier email/request-for-quote starter.
Vessel Flutes Build Packet | Slide 5 of 14

## Slide 6
Family Spec
member_id | name | target_note | target_hz | volume_cc | voicing_area_cm2 | wall_cm | estimated_neck_cm | material_path | status
VF-130-A4 | Ocarina lab body | A4 | 440.00 | 130 | 0.45 | 0.40 | 0.63 | hand-built clay or sealed proof body | first prototype
VF-95-C5 | Small vessel response body | C5 | 523.25 | 95 | 0.35 | 0.35 | 0.55 | hand-built clay | after VF-130
VF-180-G4 | Large warm vessel body | G4 | 392.00 | 180 | 0.55 | 0.45 | 0.70 | slab or slip-cast study | after shrinkage data
Vessel Flutes Build Packet | Slide 6 of 14

## Slide 7
Build Workflow
• Design and assumptions
• Source materials and hardware
• Prepare stock, fixtures, and CNC/laser/lathe setup
• Assemble, tune, finish, and validate
Vessel Flutes Build Packet | Slide 7 of 14

## Slide 8
Sourcing And BOM
• BOM gives part categories and drawing references.
• Sourcing tracks search terms, supplier candidates, price/date, lead time, substitutions.
• Visual BOM brief turns the parts list into a presentation-ready image board.
Vessel Flutes Build Packet | Slide 8 of 14

## Slide 9
Shop Packet
• Cut list for lumber/sheet/blank planning.
• Assembly manual for away-from-keyboard work.
• Validation sheet for measured dimensions, tuning, pass/fail checks.
Vessel Flutes Build Packet | Slide 9 of 14

## Slide 10
Drawings, CAD, CNC
• drawing-brief.md defines required views, dimensions, datums, sketch intent.
• cad/ holds models and design tables.
• cnc/ holds CAM, toolpaths, setup sheets, dry-run notes.
• drawings/ holds PDFs, SVGs, DXFs, drawing exports.
Vessel Flutes Build Packet | Slide 10 of 14

## Slide 11
Images And Screenshots
• Add hero render/photo, visual BOM, shop screenshots, drawing previews, validation photos in images/.
Vessel Flutes Build Packet | Slide 11 of 14

## Slide 12
Validation Plan
• A4 = 440 Hz reference check.
• Tuning targets logged in validation.csv.
• Critical dimensions verified against design sheet and CAD.
• Photos and revision notes after each major step.
Vessel Flutes Build Packet | Slide 12 of 14

## Slide 13
Open Risks / Decisions
• TBDs in design sheet and BOM.
• Supplier price/availability not yet verified.
• Generated images marked as concept placeholders.
• Empirical corrections await measured prototype data.
Vessel Flutes Build Packet | Slide 13 of 14

## Slide 14
Next Actions
• Replace TBDs with measured/source-backed values.
• Verify live supplier price and availability before buying.
• Export final drawings and visual BOM images.
• Regenerate this deck and print packet after final edits.
Vessel Flutes Build Packet | Slide 14 of 14