## Slide 1: Wooden Hang
Wooden Hang concept
Handpan-inspired wooden idiophone / resonant-vessel hybrid research packet

## Slide 2: Project Intent
Wooden Hang explores whether wood can support a lap-played circular note layout with enough pitch clarity, sustain, and ergonomic coherence to justify a new instrument family. This project does not claim that wood behaves like hammered steel or that a PANArt Hang can be reproduced by changing material alone.
The first design commitment is not “build the prettiest shell.” It is “learn the fastest honest acoustic truth.” That is why the packet leads with coupons, a single-field rig, and a three-note sector before a full 9-note layout.

## Slide 3: Why This Is Interesting
It combines wooden idiophone behavior with resonant-vessel coupling.
It keeps the handpan-like playing geometry while allowing a more repairable prototype ladder.
It could reveal a new family identity even if the final instrument sounds less like steel and more like a wooden tonal vessel.

## Slide 4: Target Family
Working name: Wooden Hang
Primary concept size: 18 in class body, 4.75 in overall height
First full target: G minor 9-note layout
Primary prototype path: replaceable top-plate hybrid over resonant bowl

## Slide 5: Governing Model
Layout drawing
The instrument is modeled as a coupled system:
local note zones behave like small plates or tongue-like hybrid regions
the bowl and port behave like a cavity resonance system
the exact tuning outcome is empirical because grain direction, glue lines, and slot geometry matter
First-order trend:
f_field ~= (kappa / (2*pi)) * (h_local / a_eff^2) * sqrt(E_eff / (rho_eff * (1 - nu^2)))

## Slide 6: Branch Comparison
Three construction paths were evaluated:
top-plate hybrid over bowl
split-shell CNC carved body in four operations
segmented or stave shell with tuned top
The hybrid path wins for first build because it preserves the circular layout while keeping the top replaceable and the tuning variables accessible.

## Slide 7: Prototype Ladder
ID | Goal | Exit gate
WHG-P0 | Coupon studies | Repeatable measurable note trend
WHG-P1 | Single-field cavity rig | One field plus one cavity coupling path
WHG-P2 | Three-note sector | Cross-talk stays manageable
WHG-P3 | Five-note subset | First playable subset
WHG-P4 | Full 9-note concept | Data-backed go/no-go on full family

## Slide 8: Note Layout
Ding: G3
Outer notes: Bb3, C4, D4, F4, G4, Bb4, C5, D5
Note sizes are marked as assumptions or derived estimates until measured
A five-note or three-note layout is allowed to become the real first instrument if the geometry demands it

## Slide 9: Manufacturing Plan
Section drawing
start with stable top stock and small coupons
build a removable-top test rig
route or build a bowl with interchangeable port sizes
escalate to sector and subset builds before the full shell
reserve the four-operation split-shell CNC path as a documented alternate

## Slide 10: CAD And CNC
cad/wooden_hang_master.scad holds the concept geometry and named inputs
SolidWorks integration files define global variables and design-table fields
CNC planning includes top routing, cavity routing, datum control, and alternate body strategies

## Slide 11: Validation Plan
Validation is designed to prove or disprove the concept, not merely describe it.
Measure:
target vs measured pitch
cents error
decay time
cross-talk
body or port resonance
moisture content
structural failures and buzz sources

## Slide 12: Risks
note fields may not sustain enough
adjacent notes may couple too strongly
the full 9-note map may be too dense for honest wooden field sizes
finish, hardware, and humidity may shift pitch more than expected
Every risk in risks.md has a concrete verification test attached.

## Slide 13: Deliverables
root-level Mode A packet with docs, CSVs, CAD/CNC, drawings, concept image, and site
print packet in Markdown and HTML
capstone deck in Markdown
binary .xlsx, .pptx, and .pdf outputs intentionally skipped because the local generator tooling is unavailable in this environment

## Slide 14: Recommended First Physical Prototype
Build WHG-P2: a three-note top-plate hybrid sector using a replaceable maple or birch-laminate top over a simple bowl with interchangeable port plugs.
Why this first:
enough geometry to test cross-talk
still cheap enough to rework
honest bridge between coupon data and a full-layout promise

## Slide 15: Next Actions
machine coupon and P1/P2 fixtures
pick two top-material systems and keep all other variables controlled
populate validation.csv immediately from the first strike tests
promote only the geometry variables that survive measurement